BILKENT UNIVERSITY
SPRING 2018
CS342: OPERATING SYSTEMS
PROJECT 3 REPORT
BERAT BİÇER - 21503050
ECEM İLGÜN – 21502157

GENERAL INFORMATION
This report includes experiment results of project 3. In the experiment, a custom test program is used for measuring stack and heap growth of its PCB. Source code of the test program is located in app.c file, while source code of the kernel module is osp3.c. Tests are performed by comparing boundaries and size of heap and stack section of PCB of the process, with respect to different parameters as follows:

- For heap, we used a struct consisting a char array of length 1024, an integer and a next pointer of the same type. Heap test depends on the number of structs allocated as nodes of a linked list.
- For stack, we used a recursive function that finds the sum of first n elements where n is the function parameter.
- For page table, we accessed top level pgd directory, and printed the valid entries it has, while mapping each bit to its corresponding content.

Results are compared by the dmesg command as follows:
First we execute the program (app.c). Program has break points where the user is required to give input from the console. This way, we allow the tester to load the kernel module osp3.ko, remove it and see the content of PCB of the process via dmesg command. Then, test program reads an input from the console and test is initialized.
First test is heap test where linked list grows from the heap until we read the char ‘*’ from the console. When the input is requested, the tester may repeat the (load kernel module – remove kernel module – dmesg for log output) cycle to see the difference from the previous log output.
After heap test is done, we deallocate the linked list and start the stack test. For stack test, tester is given the opportunity to repeat the test cycle before the test and at the largest stack point, which is the base case. Then, recursion is terminated and the test program quits.
Each time the kernel module is loaded and removed for heap/stack testing, we also receive content of pgd.

We measured heap growth for values of H = {500, 1000, 1500, 2000, 2500, 3000, 3500, 4000, 4500, 5000, 6000, 7000, 8000, 9000, 10000, 12000, 14000, 16000, 18000, 20000}, where H represents the total number of nodes allocated in the linked list. We measured the effect of total number of nodes () on heap size.
We measured stack growth for values of S = {…}, where S represents the largest integer included in the sum of S integers from 1 to S.

ENVIRONMENT AND SETUP
The experiment in which the experiments run is as follows: Ubuntu 18.04 LTS 64-bit and Windows 10 64-bit Dual Boot, Intel Core i7-6700HQ CPU @2.60 GHz x 8 with 16 GB RAM at GNOME version 3.28.1. Tests are performed using a single test file, with different parameters.

RESULTS AND DISCUSSIONS